## Slide 1: A Practical Approach for the Dynamic Analysis of Lightweight Bridges
Geoffrey Paice
Project Leader, LUSAS

## Slide 2: Overview
Trend towards more architecturally driven and aesthetically pleasing structures which can be more dynamically sensitive
Dynamic assessment therefore needs to be an integral part of the design process

## Slide 3: Dynamic Analysis Methods Required
Eigenvalue analysis
– natural frequencies
– mode shapes
Interactive Modal Dynamics (IMD)
– response of structure over time based on contributions
of a number of natural frequencies (time response)
– response of structure to dynamic loading at known
frequencies (forced response)
Step-By-Step Dynamics
– response of structure in time based on complete
structure taking all effects into account, including
nonlinear

## Slide 4: Examples of Dynamic Methods
A simple bridge will be considered with deck spans of 15m, 15m and 10m
Natural frequencies are extracted and the fundamental mode shown
Forced response at known frequencies will be shown for a 180 N load at middle of first span
Time response will be shown for a step load of 180 N at middle of first span
Two analyses will be revisited using step-by-step dynamics and compared with the IMD solutions

## Slide 5: Eigenvalue Analysis
Natural frequencies and mode shapes
Allows initial assessment of susceptibility of structure to excitation if dynamic loading has frequency at (or close to) dominant natural frequencies of the structure

## Slide 6: Interactive Modal Dynamics (IMD)
Response of the structure calculated from the modal information extracted in the eigenvalue analysis
Based on modal superposition method
Valid for elastic structures only but can be used as first approximation for nonlinear structures
Solution in both the frequency and time domains

## Slide 7: IMD Forced Response (Single Freq.)
Excitation of the structure at the fundamental natural frequency of 1.86 Hz via an IMD Loadcase
Maximum displacement under load = 0.00266 m

## Slide 8: IMD Forced Response (Freq. Range)
Using Graph Wizard and modal expansion, we can examine the response over a range of excitation frequencies
Graph of displacement response shows two clear spikes, the largest of which is associated with the fundamental frequency of 1.86 Hz (displacement = 0.00266 m)

## Slide 9: IMD Forced Response (Freq. Range)
The acceleration response can also be examined over a range of excitation frequencies
Graph shows increased number of spikes for the acceleration response. Fundamental natural frequency of 1.86 Hz still shows the largest response with acceleration in the order of 0.36 m/s2

## Slide 10: IMD Time Response To Step Load
Considering the same 180 N load applied to the structure as a step load (i.e. applied instantaneously and remains constant over all time), the IMD Loadcase and Graph Wizard modal expansion methods are available
Modal Expansion – Peak response = -0.00035 m at a time of 0.24 seconds

## Slide 11: IMD Time Response To Step Load
Using the IMD Loadcase in the time domain, a snapshot of the deformed shape can be obtained for any timestep of the analysis (Can be used to create animations)
Standard results post-processing can be performed

## Slide 12: Step-By-Step Dynamics
The same simple dynamic problems are briefly examined again using full step-by-step dynamic analyses and the solutions obtained
Forced Response At 1.86 Hz
Disp → 0.00266 m and Accel → 0.36 m/s2 agrees with IMD solution

## Slide 13: Step-By-Step Dynamics
Step Load Response
Peak response = -0.00035 m at a time of 0.24 seconds
Displacement agrees with IMD solution
Long term displacement ≈ -0.0002 m agrees with IMD solution

## Slide 14: BD37/01 Assessment
Referring to Appendix B, ‘Vibration Serviceability
Requirements For Foot And Cycle Track Bridges’
If fo (vertical) > 5 Hz (unloaded)
and fo (horizontal) > 1.5 Hz (loaded)
vibration serviceability is satisfied
If fo (vert.) ≤ 5 Hz, max. vertical accel ≤ 0.5√fo m/s2
If fo (horiz.) < 1.5 Hz, special consideration required
(Only vertical covered here)

## Slide 15: BD37/01 Assessment
For bridges whose configuration falls outside the simple rules of B.2, need to follow approach B.3 ‘General method for deriving maximum vertical acceleration’:
Passage of pulsating point load, F, across structure at
speed vt where
F = 180 sin(2πfoT) (in N), where T is time (in s)
vt = 0.9fo (in m/s)
For fo > 4 Hz, max. acceleration may be reduced by an
amount varying from zero reduction at 4 Hz to 70%
reduction at 5 Hz.

## Slide 16: BD37/01 Assessment
Due to the combined pulsating and movement of the load, the analysis can be defined through two methods:
1) Explicit definition of loading for each timestep
or
2) Load curves to define loading for each timestep
Both methods are time consuming and can be hard to check
Custom LUSAS scriptable form has been written to perform this task. Will be available via the website in an unsupported state. Source code will be available and demonstrates the LUSAS Programmable Interface

## Slide 17: BD37/01 Assessment - Example
The input data for the form is shown below
User inputs:
1) Starting loadcase, usually 1
2) Search area (Zero if no search
areas defined)
3) Fundamental natural frequency
4) Timestep for analysis
All other entries are derived from
this input and the active selection

## Slide 18: BD37/01 Assessment - Example
Features:
1) Supports search areas
2) Allows adjustment of model vertical axis from form.
Vertical axis defines direction of pedestrian load
(always applied in negative sense)
3) Pedestrian path defined from single straight line
4) Path can be reversed without redefinition
5) Generates graphs of loading vs. distance / time if
requested for inclusion in calcs, reports or QA

## Slide 19: BD37/01 Assessment - Example
Notes:
1) Only vertical effects of pedestrian loading included
2) User must ensure that Rayleigh damping coefficients
are defined for all materials in the model
3) One model and datafile will be created. If harddisk
space is limited, user can subdivide analysis into
smaller parts with restarts (see manuals)
4) Up to user to ensure timestep is sufficiently small to
capture the response of the structure
5) All timesteps are output to results (Can be modified
through editing of control for first loadcase/timestep)
6) Units must be SI: Force = N, Length = m, Mass = kg,
Time = s

## Slide 20: BD37/01 Assessment - Example
Procedure:
Take existing model
Define path for
pedestrian
Select point for dummy
load assignment(needed
to ensure all timesteps
tabulated in datafile)
Select line defining
path
Run script by loading
Run_MoveLoad-BD3701.vbs

## Slide 21: BD37/01 Assessment - Example
Enter required information
Click Ok
The script will then perform
some checking of the data,
LUSAS Modeller will remove
unwanted model data and
generate the loading histories
if requested (See next slides)
Save model and run analysis

## Slide 22: BD37/01 Assessment - Example
The pedestrian load against both time and distance are shown below
Graphs automatically generated from the script

## Slide 23: BD37/01 Assessment - Example

## Slide 24: BD37/01 Assessment - Example
Response of the structure at the midspan of the first deck. Inspection of figures shows that the structure passes the criterion with respect the the maximum vertical acceleration at this location for a pedestrian traversing along the centre of the deck
0.24 m/s2 < 0.5√fo = 0.682 m/s2

## Slide 25: BD37/01 Assessment - Example
Animation of structural response

## Slide 26: Concluding Remarks
Overview of some of the dynamic methods for lightweight bridges
Required methods are available in LUSAS
Agreement between IMD and step-by-step dynamics for elastic structure
Scriptable form for the simple definition of pedestrian passage across a structure to BD37/01, Appendix B, B.3.
Demonstration of LUSAS Programmable Interface to automate advanced dynamic modelling
Development is currently in progress to provide IMD solutions for the arbitrary moving load calculations